## Slide 1
Chapter 1 Introduction
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
Modified by Man Hon Cheung

## Slide 2: Chapter 1: introduction
our goal:
get “feel” and terminology
more depth, detail later in course
overview:
what’s the Internet?
what’s a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
security
protocol layers, service models
history

## Slide 3: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 4: What’s the Internet: “nuts and bolts” view
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Notes: 4

## Slide 5: “Fun” internet appliances
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use

## Slide 6
Internet standards
  Documents are called request for comments (RFC)
  Developed by Internet Engineering Task Force (IETF)
What’s the Internet: “nuts and bolts” view

## Slide 7: What’s the Internet: a service view
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
Q: How does one program running on one end system instruct the Internet to deliver data to another program running on another end system?
A: Internet application programming interface (API): a set of rules that the sending program must follow so that the Internet can deliver the data to the destination
  Analogous to postal service API: Write address, put a stamp,…

## Slide 8: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
Protocols define format and order of messages sent and received among network entities, and actions taken on message transmission and receipt.

## Slide 9
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?

## Slide 10: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 10

## Slide 11: A closer look at network structure:
network edge:
  hosts: clients and servers
    servers often in data centers
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 12: Access networks and physical media
Different types of access networks:
residential access networks
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 13: Home access net: digital subscriber line (DSL)
central office (CO)
ISP
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  DSL modem: takes digital data & translates it to high frequency tones for transmission over telephone wires.
  use existing telephone line by frequency division multiplexing
    voice over DSL phone line goes to telephone net
    data over DSL phone line goes to Internet
  DSL access multiplexer (DSLAM): Translate analog signals from many such houses into digital format.
DSL
modem
splitter
DSL access
multiplexer

## Slide 14
Access net: home network
to/from head end or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (100 Mbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box

## Slide 15: Enterprise access networks (Ethernet)
Ethernet is by far the most prevalent access technology in corporate, university, and home networks
10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 16: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft.)
  802.11b/g/n/ac (Wi-Fi): 11, 54, 450 Mbps, and around 1 Gbps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE
to Internet
to Internet

## Slide 17: Physical media
physical link: what lies between transmitter & receiver
Two categories of physical media:
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
least expensive and most commonly used guided transmission medium
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps

## Slide 18: Physical media: coax, fiber
coaxial cable:
two concentric copper conductors => achieve high data transmission rates
bidirectional
broadband:
  multiple channels on cable
  Hybrid fiber coax (HFC)
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 19: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
LAN (e.g., Wi-Fi)
  54 Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 20: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching vs circuit switching
    network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 20

## Slide 21: The network core
Two fundamental approaches to moving data through a network: packet switching and circuit switching.

## Slide 22: Circuit switching
Circuit switching: end-end resources are reserved for communication between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks

## Slide 23: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:

## Slide 24: Packet-switching
Packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 25: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 26: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 27: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  queuing delay: packets will queue, wait to be transmitted on link
  Packet loss: packets can be dropped (lost) if memory (buffer) fills up

## Slide 28: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 29: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
…..
* Check out the online interactive exercises for more examples

## Slide 30
Binomial distribution

## Slide 31
For packet switching:
Adv: great for bursty data
  resource sharing
  simpler, no call setup
Dis: excessive congestion possible → packet delay and loss
  protocols needed for reliable data transfer, congestion control
Is packet switching a “slam dunk winner?”
reserved resources (circuit switching) versus on-demand allocation (packet switching)
Packet switching versus circuit switching

## Slide 32
Circuit switching versus Packet switching
circuit switching
packet switching

## Slide 33: Internet structure

## Slide 34: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 35: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 36: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 37: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP

## Slide 38: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C

## Slide 39: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point

## Slide 40: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
ISP B
ISP A
ISP C
IXP
IXP
regional net

## Slide 41: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network

## Slide 42: Internet structure: network of networks!
Small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 43: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 43

## Slide 44: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (transmission delay)
packets queueing (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 45: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop

## Slide 46
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Four sources of packet delay
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
* Check out the Java applet for an interactive animation on trans vs. prop delay: https://wps.pearsoned.com/ecs_kurose_compnetw_6/216/55463/14198702.cw/index.html
Notes: 46

## Slide 47: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec = 2 min
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 48: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes 1 min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 49: Queueing delay (revisited)
R: link bandwidth (bps = bits/sec)
L: packet length (bits/packet)
a: average packet arrival rate (packets/sec)
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
traffic intensity = La/R